## Slide 1
SYMBIOSIS INSTITUTE OF TECHNOLOGY, PUNE | IEEE Student Branch
SOLUTION ARCHITECTURE - HOW IT WORKS
1. OPTICAL INGESTION & TRIGGER
Conveyor proximity sensor triggers Global Shutter 1080p camera under fixed, diffused LED lighting.
2. SPATIAL NORMALIZATION
OpenCV bilateral filtering, ROI cropping, and Planar Homography matrix alignment eliminate vibration.
3. TIER 1: ZERO-SHOT SKU ROUTING
OpenAI CLIP (ViT-B/32) computes cosine similarity against enrolled SKU visual prototypes. - Sim < 0.60 -> Unknown Object Guardrail (Line Hold / Prompt Onboarding) - Sim >= 0.60 -> Target SKU Identified (e.g., 'SKU_Bolt_M8')
4. TIER 2: MEMORY BANK SCORING
Dispatches to Registry['SKU_Bolt_M8']. Computes patch Euclidean distance to 10% Coreset memory bank. - Latency < 14 ms via TensorRT INT8 quantization on edge hardware.
5. 3-WAY DECISION & ACTUATION
- Score < t_low -> PASS: Unit proceeds nominally down conveyor - t_low <= Score <= t_high -> REVIEW: Escalated to human QA queue - Score > t_high -> REJECT: Fires Modbus TCP trigger to pneumatic diverter arm
6. INSPECTABLE XAI & TELEMETRY
Side-by-side nearest nominal patch retrieval from memory bank + real-time drift tracking dashboard.

## Slide 2
SYMBIOSIS INSTITUTE OF TECHNOLOGY, PUNE | IEEE Student Branch
AI INNOVATION & TECH STACK
CORE ANOMALY AI
PatchCore (Coreset Memory Bank)
Zero-Defect Calibration: Learns exclusively from 20-30 nominal parts using minimax facility location, eliminating the need for labeled defect datasets.
ZERO-SHOT ROUTING
OpenAI CLIP (ViT-B/32)
Zero-Shot Multi-SKU Dispatch: Uses cosine similarity to route frames to component-specific memory banks; halts lines on unrecognized parts.
INSPECTABLE XAI
Patch-Level Metric Retrieval
Nearest-Neighbor Visual Proof: Replaces uncalibrated attention maps with exact Euclidean distance heatmaps and displays side-by-side nominal reference patches.
EDGE ACCELERATION
NVIDIA TensorRT (INT8)
Sub-14ms Execution: Layer fusion and symmetric integer quantization to sustain >70 FPS on edge hardware (NVIDIA Jetson / Industrial IPC).
VISION PREPROCESSING
OpenCV & Spatial Transformers
Perspective Correction: Homography matrix calibration and sub-pixel edge profiling to isolate regions of interest and eliminate conveyor vibration.
CONTROL & TELEMETRY
FastAPI, Streamlit, Modbus TCP
Closed-Loop Actuation: Delivers real-time pass/review/reject telemetry and fires direct PLC signals to pneumatic rejection diverters.